## Slide 1
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Homework: Derive the following expression for the derivative of the inverse mapping

## Slide 2
Differential Calculus| Important Expressions
Arun Das | Waterloo Autonomous Vehicles Lab
(1) Box-plus and box-minus
(2) Rodriguez Formula
(3) Inverse Identity
(4) Adjoint Related Identity
(5) anticommutative

## Slide 3
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Homework: Derive the following expression for the derivative of the inverse mapping

## Slide 4
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Formulate a method to interpolate between two Transformation matrices.

## Slide 5
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Formulate a method to interpolate between two Transformation matrices.
Consider linear interpolation:
Can we do something similar for SO(3) or SE(3)?

## Slide 6
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Formulate a method to interpolate between two Transformation matrices.
Consider linear interpolation:
Can we do something similar for SO(3) or SE(3)?

## Slide 7
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Define the following interpolation scheme:
Note that:

## Slide 8
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Define the following interpolation scheme:
Note that:

## Slide 9
Homework|
Arun Das | Waterloo Autonomous Vehicles Lab
Note that we always have closure with this scheme
Essentially interpolation on the Lie Algebra

## Slide 10
Homework |
Read and Summarize:
SURF Detector and Descriptor
ORB Detector and Descriptor
Jason Rebello | Waterloo Autonomous Vehicles Lab

## Slide 11
SURF Detector | Integral Image
Create: 16 + 12 - 7 + 3 = 24
Create: 16 + 23 - 13 + 6 = 32
Query: 64 + 5 - 14 - 16 = 39
same as 6+3+6+2+5+2+6+3+6 = 39
Jason Rebello | Waterloo Autonomous Vehicles Lab

## Slide 12
SURF Detector | Speeded Up Robust Features
Gaussian Partial Derivatives
Box Filter Approximations
Hessian Matrix and Determinant
Scale space analysis
Lyy
Lxy
Dyy
Dxy
Jason Rebello | Waterloo Autonomous Vehicles Lab

## Slide 13
SURF Descriptor |
Haar Wavelets
Dominant Orientation
SURF Descriptor
Each patch is 4 dimensional vector
16 Patches give 64 Dimensional Vector
Sign of Hessian Matrix for black vs white blobs
Black vs White blobs
Jason Rebello | Waterloo Autonomous Vehicles Lab

## Slide 14
ORB Detector | Oriented fast and Robust Brief
FAST corner Detector
Harris Corner Measure
FAST detected at multiple levels in the Pyramid for Scale Invariance
BRIEF: Binary Robust Independent Elementary Features
Random Selection of pairs of Intensity Values
Fixed sampling Pattern of 128, 256 or 512 pairs
Hamming Distance to compare descriptors (XOR)
Jason Rebello | Waterloo Autonomous Vehicles Lab

## Slide 15
ORB Descriptor |
Jason Rebello | Waterloo Autonomous Vehicles Lab
Patch moments
Center of Mass
Orientation
Angle Calculation
Learning the pairs
300K Keypoints
205590 Possible Tests
256 dimensional descriptor