## Slide 1: Kinematics: Part 1
Arun Das | Waterloo Autonomous Vehicles Lab
Arun Das
29/03/2017

## Slide 2
Kinematics Overview | Outline: Part 1
Arun Das | Waterloo Autonomous Vehicles Lab
Kinematics: Motivation
Rotation Representation
Pose Representation
Parameterizations
Matrix Lie Groups, SO(3) and SE(3)
Kinematics Lab Standards
  Documentation
  Code

## Slide 3
Kinematics Overview| Motivation
Arun Das| Waterloo Autonomous Vehicles Lab
How do we map and analyze quantities between co-ordinate frames?

## Slide 4
Kinematics Overview | Rotations – SO(3)
Arun Das| Waterloo Autonomous Vehicles Lab
Rotations are part of a special group
  det =1
  Orthogonal matrix
SO(3) or Special Orthogonal Group
Manifold, not a vector space!

## Slide 5
Kinematics Overview | Transformation – SE(3)
Arun Das| Waterloo Autonomous Vehicles Lab
An element of a Euclidean Group, E(n) is a translation and an orthogonal transformation A,
When A is from SO(3), we get the Special Euclidean Group
Homeomorphic to

## Slide 6
Kinematics Overview | Rotations – Euler Angles
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 7
Kinematics Overview | Rotations – Gimbal Lock
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 8
Kinematics Overview | Rotations – Quaternions
Arun Das| Waterloo Autonomous Vehicles Lab
Alternate rotation parameterization
Over parameterized
Solved by adding norm constraint

## Slide 9
Kinematics Overview | Definitions: Manifold
Arun Das| Waterloo Autonomous Vehicles Lab
A manifold locally looks like an open subset of

## Slide 10
Kinematics Overview | Definitions: Tangent Space
Arun Das| Waterloo Autonomous Vehicles Lab
A vector space that best approximates the manifold about a point, tangent to the Manifold at the point.

## Slide 11
Kinematics Overview | Definitions: Group
Arun Das| Waterloo Autonomous Vehicles Lab
A Group is a set, G, together with an operator, known as the group law, that can combine two elements in the group to form a third.
Must satisfy four axioms
  Closure:
  Associativity:
  Identity Element:
  Inverse Element:

## Slide 12
Kinematics Overview | Definitions: Lie Group
Arun Das| Waterloo Autonomous Vehicles Lab
A Lie Group is a group if it is a smooth manifold such that the maps
are smooth
Rotations SO(3) and Transformations SE(3) are examples of Lie Groups

## Slide 13
Kinematics Overview | SO(3)
Arun Das| Waterloo Autonomous Vehicles Lab
Not all 3x3 matrices are members of SO(3)
Recall we have constraints on the rotation matrix.
Locally, the group is 3 dimensional.
3 dimensional manifold embedded in
What matrices in SO(3) differ from the identity by a small amount?

## Slide 14
A Rotation matrix near identity:
The rotation times its transpose is identity:
Kinematics Overview | SO(3)
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 15
Ignoring second order terms:
Six independent constraints:
Only need three parameters (b,c,f)
Kinematics Overview | SO(3)
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 16
Any rotation near the identity looks like
G1,G2,G3 are called Generators
Kinematics Overview | SO(3)
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 17
All group elements have a tangent space. Together, known as a Tangent Bundle
Kinematics Overview | Tangent Space and the Lie Algebra
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 18
All group elements have a tangent space. Together, known as a Tangent Bundle
Kinematics Overview | Tangent Space and the Lie Algebra
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 19
All group elements have a tangent space. Together, known as a Tangent Bundle
Kinematics Overview | Tangent Space and the Lie Algebra
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 20
All group elements have a tangent space. Together, known as a Tangent Bundle
Kinematics Overview | Tangent Space and the Lie Algebra
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 21
Let’s re-visit our SO(3) example
If we let the generator coefficients to become, non infinitesimal, we get a 3-dimensional space that is tangent to the Identity element. Note that the generators form a basis for this space.
Kinematics Overview | Tangent Space and the Lie Algebra
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 22
2D visualization
The tangent space at the identity element is given a special designation: the Lie Algebra of the group,
and is denoted by
Kinematics Overview | Tangent Space and the Lie Algebra
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 23
Kinematics Overview | Lie Algebra: Properties
Arun Das| Waterloo Autonomous Vehicles Lab
The Lie Algebra is a vector space, along with a binary operation called the Lie Bracket
Must satisfy full list of axioms associated with Lie Bracket (https://en.wikipedia.org/wiki/Lie_algebra)

## Slide 24
The tangent space at the identity element (Lie Algebra) is isomorphic to the tangent space of the other group elements.
Kinematics Overview | Tangent Space and the Lie Algebra
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 25
Define a tangent space element at the identity:
Kinematics Overview | Relationship of Lie Algebra to Lie Group
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 26
The differential equation that relates the tangent spaces:
Kinematics Overview | Relationship of Lie Algebra to Lie Group
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 27
Solve the differential eqn with initial condition
Kinematics Overview | Relationship of Lie Algebra to Lie Group
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 28
We call this relationship between the Lie Algebra and Lie group the exponential map. For SO(3), when t=1
Kinematics Overview | Relationship of Lie Algebra to Lie Group
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 29
Visual example of exponential map
As n grows, quantity inside brackets becomes member of SO(3). Multiplication n times also gives member of SO(3). Successive approximations:
Kinematics Overview | Exponential Map
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 30
For SO(3), the Lie Algebra is the set of all skew-symmetric matrices
This gives us a very nice parameterization for SO(3), using an element in to represent an element in SO(3).
Kinematics Overview | Parameterization
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 31
Exponential Map for SO(3) has a closed form solution, called the Rodrigues formula.
We can also invert the exponential map using the logarithmic map.
Kinematics Overview | Parameterization
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 32
We can use a similar derivation to get the generators of SE(3)
G1,G2,G3 are generators for the translations, G4,G5,G6 are the generators for the rotation.
Kinematics Overview | Transformations: SE(3)
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 33
The exponential map for SE(3) also has a closed form:
Kinematics Overview | Transformations: SE(3)
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 34
The logarithmic map for SE(3) also has a closed form:
Kinematics Overview | Transformations: SE(3)
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 35
Kinematics Overview | SO(3) and SE(3) Summary
Arun Das| Waterloo Autonomous Vehicles Lab
 | Rotation | Transformation
Matrix | 3x3 matrix | 4x4 matrix
Lie Group | SO(3) | SE(3)
Lie Algebra | so(3) | se(3)
Tangent vectors | “angular velocities” | “twist”

## Slide 36
Kinematics Overview| Kinematics Standards
Arun Das| Waterloo Autonomous Vehicles Lab
A summary of 2014 ICRA workshop presentation by Paul Furgale, “Representing Robot Pose: The good, the bad, and the ugly”.
Notation traced back to this book: Elastic Multibody Dynamics -- A Direct Ritz Approach
Full slides: http://paulfurgale.info/news/2014/6/9/representing-robot-pose-the-good-the-bad-and-the-ugly

## Slide 37
Kinematics Overview| Pain Points: three value problem
Arun Das| Waterloo Autonomous Vehicles Lab
Given a 3 value parameterization, how much do we really know?

## Slide 38
Kinematics Overview| Pain Points: three value problem
Arun Das| Waterloo Autonomous Vehicles Lab
There are 12 valid combinations of rotations
  z-x-z, x-y-x,y-z-y,z-y-z…
  x-y-z, y-z-x, z-y-x, x-z-y…
Each can be either active or passive

## Slide 39
Kinematics Overview| Pain Points: Active vs Passive Rotations
Arun Das| Waterloo Autonomous Vehicles Lab
Active Rotation (left): Point changes location
Passive Rotation (right): Change of co-ordinate frame

## Slide 40
Kinematics Overview| Pain Points: Rotation Direction
Arun Das| Waterloo Autonomous Vehicles Lab
From Map to Vehicle frame? Or from Vehicle to Map frame?

## Slide 41
Kinematics Overview| Pain Points: Parameter Ordering
Arun Das| Waterloo Autonomous Vehicles Lab
What is the ordering of the parameters?
x y z
z y x
y x z
y z x
z x y
z y x

## Slide 42
Kinematics Overview| Pain Points: Units
Arun Das| Waterloo Autonomous Vehicles Lab
Degrees or Rads?
Deg
Rad

## Slide 43
Kinematics Overview| Pain Points: Units
Arun Das| Waterloo Autonomous Vehicles Lab
(12) valid rotation combinations?
(2) active or passive?
(2) rotation direction
(6) parameter ordering
(2) units

## Slide 44
Kinematics Overview| Pain Points: three value problem
Arun Das| Waterloo Autonomous Vehicles Lab
Given a 3 value parameterization, how much do we really know?

## Slide 45
Kinematics Overview| Pain Points: three value problem
Arun Das| Waterloo Autonomous Vehicles Lab
Given a 3 value parameterization, how much do we really know?
VERY LITTLE:
576 different combinations

## Slide 46
Kinematics Overview| Pain Points: Quaternion Ordering
Arun Das| Waterloo Autonomous Vehicles Lab
Scalar first or scalar last?
Scalar first
Scalar Last

## Slide 47
Kinematics Overview| Pain Points: Quaternion handedness
Arun Das| Waterloo Autonomous Vehicles Lab
JPL vs Hamilton?
  Hamilton: Right handed rotations
  JPL: Left handed rotations

## Slide 48
Kinematics Overview| Axis Angle: Any better?
Arun Das| Waterloo Autonomous Vehicles Lab
Still investigating in more detail
exp map is not one-to-one, will map rotations in multiples of 2pi to same group element
  Also need to be careful when rotation magnitude is close to zero

## Slide 49
Kinematics Overview| Moose Standards
Arun Das| Waterloo Autonomous Vehicles Lab
Frame | Description | Kinematics Tag
Camera | Camera Lens Optical Center | C
Point | Landmark (Point) Frame | P
Vehicle | Centre of Back Axle | V
IMU | IMU Origin | I
GPS | Antenna Phase Center | G
Lidar | Local Lidar Point Frame | L
Encoder | About axis of rotation | E
Radar | Radar Center | R
ECEF | Earth Centered Earth Fixed | F
Map | Localization Map Frame | M

## Slide 50
Kinematics Overview| Kinematics Standards: Frame Diagram
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 51
Kinematics Overview| Kinematics Standards: Vector Decoration
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 52
Kinematics Overview| Kinematics Standards: Vector Decoration
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 53
Kinematics Overview| Kinematics Standards: Vector Rotation
Arun Das| Waterloo Autonomous Vehicles Lab
Be very clear in terms of rotation direction

## Slide 54
Kinematics Overview| Kinematics Standards: Vector Rotation
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 55
Kinematics Overview| Kinematics Standards: Pose Transformations
Arun Das| Waterloo Autonomous Vehicles Lab
Be very clear about the pose transformation direction

## Slide 56
Kinematics Overview| Kinematics Standards: Pose Transformations
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 57
Kinematics Overview| Kinematics Standards: Code implementation
Arun Das| Waterloo Autonomous Vehicles Lab

## Slide 58
Kinematics Overview | Preview for Part 2
Arun Das | Waterloo Autonomous Vehicles Lab
In depth derivations of the closed forms for exp and log maps on SO(3) and SE(3)
Adjoint mapping and representations
Defining “distance” between group elements
Differential Calculus on SO(3) and SE(3)
Implementation using wave::kinematics
Building residual terms using wave::kinematics